Pennsylvania

| Record Keeping | Must keep daily records of tests and of the operation of the facility on forms satisfactory to the Department and file these forms monthly (or more often if required) with the appropriate office of the county health department |
| --- | --- |
| Water Testing Frequency | Must test water at least twice daily when the pool is in use or more often if required by the local Health Department Must take a water sample at least one week before opening and then once a week to be tested by a laboratory (that is approved) |
| Chlorine/Bromine Levels (Min-Max) | Chlorine—free chlorine residual must be a minimum of .4 ppm in all parts of the pool (Chester County—minimum of 2.0/maximum of 5.0) Other disinfectants can be used with approval |
| pH Levels (Min-Max) | pH—7.2-8.2 (Chester County—7.2-7.6) |
| Chlorine Test Kit Requirements | DPD |
| pH Test Kit Requirements | No standard |
| Cyanuric Acid Levels (Min-Max) | Chester County—CYA not over 50 ppm, others not specified |
| Water Clarity | Must be able to see a black disk, 6 inches in diameter when placed on the bottom of the pool at the deepest point |
| Turnover Rate | Wading Pool—not longer than 2 hours Other Pools—not longer than 8 hours |
| Bather Load (per bather) | The bather load of the recreational swimming establishment may not exceed the maximum bather load as defined in the permit application |
| Depth Markings | Not specified |
| Total Alkalinity | 60-180 ppm |
| CPO® Required | No. It is required to have a certified pool operator for all public swimming pools in Allegheny County and recommended in Bucks, Chester and Montgomery Counties |
| Lifeguard Requirements | Recognized Agencies: American Red Cross YMCA Ellis and Associates Required Number of Guards: At least one certified lifeguard for every 4000 square feet of water surface area, plus one certified lifeguard for any fraction thereof, equal to or greater than 1000 square feet shall be on duty at the waterside at all times the facility is open. At no time shall there be fewer than two certified lifeguards present and available to aid bathers Owners may reduce the water surface area by closing sections of the pool with a rope or float line (includes total water surface including wading pools) Under circumstances when the ability of the lifeguard to survey 4000 SF of water surface is impaired (due to size of pool, shape or both) additional lifeguards may be needed At least one lifeguard must be present for swim meets, swim practices, swim lessons or other special events at least one lifeguard must be present Wading Pools: the lifeguard must have an unobstructed view of the wading pool or an additional lifeguard will be needed Diving Boards/slides: the lifeguard must be stationed within 50 feet; if a lifeguard is to monitor both areas they must be within 50 feet; if these are physically separated they must have a lifeguard stationed to them exclusively [this surface area will not be included in calculations for the rest of the facility in determining additional guards for the other pools(s)] |
| Equipment Requirements | Reaching devices: One or more (poles, ropes) Flotation devices: One or more (lifejackets or flotation devices that can support an adult in the water) First Aid Kit: a standard 24 unit first aid kit, readily accessible Chester County: backboard with head immobilizer and straps |
| Bather Health | Persons with signs of illness or disease or with skin rashes or sores or with bandages shall be excluded from swimming except when certified by a physician not to have a disease that is in a communicable stage |